## Slide 1: Minnesota Stormwater Manual Pretreatment Updates
June 18, 2019

## Slide 2: Overview
Project Team & Roles
Overview of Pretreatment Work
Pretreatment Settling Practices Updates
Pretreatment Sizing Recommendations
Pretreatment Case Studies

## Slide 3
Project Team & Roles
3
Katy Thompson, PE | RESPEC
  Project Manager, Pretreatment Case Studies, Pretreatment Sizing
Scott Struck, PhD, PE | Geosyntec
  Pretreatment Settling Practices and BMP Selection Tool
John Gulliver, PHD, PE
  Pretreatment Sizing
Andy Erickson, PhD, PE
  Filter Strips and Stormwater Manual update

## Slide 4: Overview of Pretreatment Work
MN Stormwater Manual Update
New Features
Links

## Slide 5: Overview of Pretreatment Work
Pretreatment (overview)
  Importance
  Methods
  Practices
    Settling devices
    Screens
    Vegetated filter strips
  Cost considerations
  Applicability
  Compatibility with downstream structural stormwater BMPs
30+ cited references
  https://stormwater.pca.state.mn.us/index.php?title=Overview_and_methods_of_pretreatment
Dr. Andy Erickson, PE

## Slide 6: Overview of Pretreatment Work
Pretreatment Settling Devices
  Processes
  Applicability and suitability
    Cold climate
    Retrofit
    Ultra-urban
  Permit applicability
  Advantages and limitations
  Water quantity treatment (volume reduction)
  Water quality treatment (performance)
  Certification programs
  https://stormwater.pca.state.mn.us/index.php?title=Overview_and_methods_of_pretreatment
Dr. Andy Erickson, PE

## Slide 7: Overview of Pretreatment Work
Pretreatment Screens
  Processes
  Applicability and suitability
    Cold climate
    Retrofit
    Ultra-urban
  Permit applicability
  Advantages and limitations
  Water quantity treatment (volume reduction)
  Water quality treatment (performance)
  https://stormwater.pca.state.mn.us/index.php?title=Overview_for_pretreatment_screens
Dr. Andy Erickson, PE

## Slide 8: Overview of Pretreatment Work
Pretreatment Vegetated Filter Strips
  Processes
  Applicability and suitability
    Cold climate
    Retrofit
    Ultra-urban
  Permit applicability
  Advantages and limitations
  Water quantity treatment (volume reduction)
  Water quality treatment (performance)
  https://stormwater.pca.state.mn.us/index.php?title=Overview_for_pretreatment_vegetated_filter_strips
Dr. Andy Erickson, PE

## Slide 9: Overview of Pretreatment Work
Design, Construction, Operation and Maintenance: Pretreatment Vegetated Filter Strips
  Design criteria
  Construction specifications
  Operation and maintenance
+20 cited references
  https://stormwater.pca.state.mn.us/index.php?title=Design,_construction,_operation_and_maintenance_specifications_for_pretreatment_vegetated_filter_strips
Dr. Andy Erickson, PE

## Slide 10: Pretreatment Settling Practices
Pretreatment Settling Practices Updates
Pretreatment Selection Tool
Demonstration

## Slide 11: Pretreatment Settling Practices Updates
11
Pretreatment is a required part of infiltration and filtration practices covered under the Minnesota Construction Stormwater General Permit
Objective:
  Provide design criteria and considerations, construction guidelines, and maintenance recommendations for stormwater pretreatment controls
three general types of pretreatment practices
  Settling Devices
  Screens
  Vegetated Filter Strips

## Slide 12: Pretreatment Settling Practices Updates
12
Detailed pretreatment functional process for pollutant removal
List of (Primary) Processes
  Hydrodynamic Separation Devices
  Screening and Straining Devices
  Above Ground and Below Grade Storage and Settling Systems
  Filtration Practices
  Other Water Quality Devices
Organization
  Each functional process section is subdivided into:
    Pretreatment Overview
    Process Summary and Pollutant Removal
    System Design and Sizing Information
    Installation Recommendations, Inspection, and Operation and Maintenance
  Numerous references to manufacturer or assessment websites to assist with design, construction, performance, and operation and maintenance

## Slide 13: Hydrodynamic Separation Devices
13
Pretreatment Wiki Page
Hyperlinked Text

## Slide 14: Hydrodynamic Separation Devices
14
Flow-through, often proprietary structures that establish a high-speed rotating flow within a cylindrical chamber
  Treatment Mechanisms
  General Pollutants Removed

## Slide 15: Hydrodynamic Separation Devices
15
System Sizing and Design Information
  Typical Land Use Applied
  Compatible Downstream Practice
  Sizing Calculations
  Inlets and Outlets
  Openings
  Flow Diversion Structures

## Slide 16: Hydrodynamic Separation Devices
16
Installation Recommendations, Inspection, and Operation and Maintenance
  Installation Considerations
  Inspection Frequency
  Typical Maintenance
  Public/ Private Considerations
  Minimize Maintenance
  Cost Considerations
Hyperlinked Text
Linked References

## Slide 17: Hydrodynamic Separation Devices
17
Navigation Links to Tabular Information

## Slide 18: Screening and Straining devices
18

## Slide 19: Above ground and below grade storage and settling devices
19

## Slide 20: Filtration devices and practices
20

## Slide 21: Other pretreatment water quality devices and practices
21

## Slide 22: Pretreatment Selection Tool
22

## Slide 23: Filtering Categories
23
System Sizing and Design Information (select up to four)
  General Pollutant Type
  Downstream BMP Protected
  Drainage Area
  Space Requirements

## Slide 24: General Pollutant Type
24
  Mineral and Organic Solids
  Floatables
  Oil and Grease

## Slide 25: Downstream BMP being Protected
25
  Filtration
  Infiltration
  Storage

## Slide 26: Drainage Area
26
  Large
  Medium
  Small
  Extra Small

## Slide 27: Space Requirements
27
  Above Ground - Large
  Above Ground - Small
  Underground – Large and/or Deep
  Underground – Small and/or Shallow

## Slide 28: Results
28
  Equipment cost (e.g., hire a professional or specialized equipment
  Is confined space entry certification may be required?
  Labor hours
  Inspection frequency

## Slide 29: Filtered Data Results
29

## Slide 30: Practice Details
30
  Text Information
  Comparative Tables

## Slide 31: Pretreatment Sizing Recommendations
State Comparisons
Preliminary Sizing Recommendations
  Rock Filter Strip
  Vegetated Filter Strip
  Sump

## Slide 32: Pretreatment Around the Country
32
Reviewed all 50 states’ stormwater permits and manuals (if exist)
Not all states explicitly require pretreatment
A lot of variation in design criteria
https://stormwater.pca.state.mn.us/index.php?title=Stormwater_manuals

## Slide 33: Forebays
33

## Slide 34: States with Detailed Design Criteria
34

## Slide 35: Forebay findings
35
sizing Criteria Examples include:
  0.1-in of runoff per impervious acre
  1- to 10% of water quality volume
  1- to 40% of BMP total runoff volume
  10 storms per year * Sanded Area (ac) * 500lb/ac-storm / 90 lb/cf
Minnesota Stormwater Manual:
  10% of water quality volume and 4- to 6-ft deep, recommended

## Slide 36: Pretreatment Sizing Recommendations
Why is sizing important for the manual?
  Many smaller treatment facilities (bioretention/biofiltration or rain gardens) do not have a pretreatment sizing criteria and are too small to justify hiring an engineer.
  Larger treatment practices (e.g., ponds, infiltration basins, roadside swales) could use a simple preliminary design methodology for pretreatment.
What are we considering?
  Preliminary sizing criteria is being developed from the watershed’s impermeable area, the design storm intensity, the settling velocity of the targeted particle size, and the fraction of that size to be removed.
What will be the result?
  Sizing criteria for the area of filter strips and the surface area of basins, and recommendations on the depth of basins.
36

## Slide 37: Pretreatment Case Studies
Participants
Example Case Studies
  Vegetated Filter Strip
  Rock Filter Strip
  Forebay
Links

## Slide 38: THANK YOU!!!
38

## Slide 39
Vegetated Filter Strips
City of Burnsville
AT-A-GLANCE
Provide pretreatment from street runoff prior to entering residential raingardens
Vegetated filter strips have a lifespan of 5 to 7 years, but have prolonged the lifespan and reduced maintenance of the rain gardens
Incorporate “drop waterfalls” at curb cutout to slow the speed and reduce erosion potential of the runoff entering the vegetated filter strip.

## Slide 40
Rock Filter Strips
City of Fridley
AT-A-GLANCE
Provide pretreatment from street runoff prior to entering curb-cut bioswales
Blocked inlets can cause stormwater to bypass the basin.
Initial rocks in filter strips were too small, which resulted in rocks getting carried into the bioswale during larger rain events.
Trial-and-error showed Class I riprap was the appropriate rock size (3 – 6 inches in diameter)

## Slide 41
Rock Filter Strips
City of Fridley
41
AT-A-GLANCE
Regular maintenance has prolonged lifespan and function
Delegated maintenance responsibilities to contractor resulted in more consistent maintenance & better results.

## Slide 42
Sediment Forebay
City of South St. Paul/Dakota County SWCD
AT-A-GLANCE
Forebay cell designed to promote the longevity of the iron-enhanced sand filter cell
Level spreader weirs distribute flows evenly into pretreatment cell
Turfstone pavers facilitate sediment maintenance

## Slide 43
Sediment Forebay
City of South St. Paul/Dakota County SWCD
AT-A-GLANCE
The turfstone and weir design are successfully capturing large amounts of sediment
Forebay has experienced significant surface ponding
Future designs would include underdrains to facilitate proper drainage with poor/compacted soils
Vaccuum turfstone to remove layer of fine sediment at paver surface and replace with washed sand during regular maintenance.

## Slide 44: PRETREATMENT CASE STUDIES
44
Full case studies can be found at:
https://stormwater.pca.state.mn.us/index.php?title=Case_studies_for_pretreatment

## Slide 45: Thank you & Questions?
Katy Thompson
katy.thompson@respec.com
651.305.2275
Scott Struck
SStruck@Geosyntec.com
303.586.8194
John Gulliver
gulli003@umn.edu
Andy Erickson
eric0706@umn.edu